## Slide 1: CPF Tutorial
Yanqing Zhang, Yousef Shaksheer

## Slide 2: CPF Tutorial
First, you will need to create a .cpf file. Here we will use “synth.cpf” as an example, which is a script for power-gating in the synthesis flow.

## Slide 3: CPF Tutorial
Next, we will break down the writing of the .cpf file into specific steps. Note that you will only need to write the CPF file once, and it will be used for the ENTIRE flow. In other words, once written, there is no need to change it. We start by setting the cpf version:
set_cpf_version 1.1
…
…
…
For a complete list of supported CPF commands and CPF user guide, refer to
documentation at:
/app/cadence/RC81/doc/cpf_ref
/app/cadence/RC81/doc/cpf_user

## Slide 4: CPF Tutorial
We define the technology to be used in our design:
set_cpf_version 1.1
#################################################
# Technology part of the CPF
#################################################
# define the library sets, a library ‘set’ is often a set of .lib’s that have been characterized at the same
#voltage, here, both the standard cell library SubVT_400mV.lib and the header library headers.lib have
#been characterized at 400mV.
define_library_set -name CORE9GPLL -libraries {SubVT_400mV.lib headers.lib}
# define the isolation cells, also define the enable pin and enable condition for isolation cells
#define_isolation_cell -cells ISOLN* -enable ENbar -valid_location on
# define the always on cell
# define the state retention cell
# define the power switch cells, defines names of the headers used, the power on condition, and the
#name of the power rails that it will be switching between
define_power_switch_cell -cells "HDX2 HDX4 HDX8 HDX16 HDX32 HDX64" \
-stage_1_enable !_EN -type header -gate_bias_pin gnd -power_switchable VDDS -power vdd \
-on_resistance 100.0
…
…

## Slide 5: CPF Tutorial
We continue to define design parameters for our design, this means telling the tools, through the CPF file, which part of the design is to be low-power implemented, which instances belong to which power domain, and the different power modes that exist
…
…
# identify the design for which the CPF file is created, also define the units for numbers
set_design PIC_ROM
set_power_unit nW
set_time_unit ns
# create power domains, a power domain is a group of instances that have the same power switching characteristics. Also defines which instances are in each power domain,
#and the condition where they switch to that power domain
create_power_domain -name PD1 -default
create_power_domain -name PD2 -instances {ALU} \
-shutoff_condition {MCLR} -secondary_domains PD1
# create nominal conditions, gives a name to each voltage island. This means that off=0, on=0.4V
create_nominal_condition -name off -voltage 0
create_nominal_condition -name on -voltage 0.4
# create power modes, a power mode specifies which voltage island each power domain will be operating in
create_power_mode -name PM1 -domain_conditions {PD1@on PD2@on} -default
create_power_mode -name PM2 -domain_conditions {PD1@on PD2@off}
# associate library sets with nominal conditions
update_nominal_condition -name on -library_set CORE9GPLL
# create rules for isolation logic insertion
# create rules for state retention insertion
# create rules for power switch insertion, defines the primary power net, and the virtual power rails associated with each power switch rule
create_power_nets -nets vdd -voltage 0.4
create_power_switch_rule -name SW1 -domain PD2 -external_power_net vdd

## Slide 6: CPF Tutorial
Specify information for synthesis, this includes power and leakage targets, timing constraints, and IR drop and recovery time for power switches
…
…
# specify power targets, if not specified, you may specify these with commands in
#synthesis
#set_power_target -leakage 30 -dynamic 250
# specify timing constraints, attaches .sdc file with a power mode
update_power_mode -name PM1 -sdc_files PIC_ROM_mapped.sdc
update_power_mode -name PM2 -sdc_files PIC_ROM_mapped.sdc
# update the rules with implementation info
#update_isolation_rules -names iso1 -location to -cells ISOLNX2M
#update_isolation_rules -names iso2 -location to -cells ISOLNX2M
update_power_switch_rule -name SW1 -cells "HDX2 HDX4 HDX8 HDX16 HDX32 HDX64" -enable_condition_1 !MCLR -prefix CDN_ -average_ir_drop_limit 0.020 -peak_ir_drop_limit 0.040
…
…

## Slide 7: CPF Tutorial
Finally, we end by specifying information for physical implementation, including the connecting of power/ground nets, and process corners
…
…
# declare power and ground nets, including virtual rails
create_power_nets -nets VDDS -internal -average_ir_drop_limit 0.020 -peak_ir_drop_limit 0.040
create_ground_nets -nets gnd -voltage 0
# (optional) create global connections
create_global_connection -net vdd -pins vdd
create_global_connection -net gnd -pins gnd
# add implementation info for power domains
update_power_domain -name PD1 -primary_power_net vdd -primary_ground_net gnd
update_power_domain -name PD2 -primary_power_net VDDS -primary_ground_net gnd -transition_cycles 2.0
update_power_mode -name PM2 -average_ir_drop_limit PD2@0.020 -peak_ir_drop_limit PD2@0.040
# create operating corners
create_operating_corner -name WC \
-process 1 -temperature 125 -voltage 0.4 -library_set CORE9GPLL
# create analysis views
create_analysis_view -name AV_PM1 -mode PM1 \
-domain_corners {PD1@WC PD2@WC}
# indicate when the power information for the design ends
end_design

## Slide 8: CPF Tutorial
Now we’ve completed the .cpf file. To incorporate the .cpf file in the synthesis script, we will have to add a few more commands to the synthesis script, as depicted below:
…
…
set_attribute drc_first true
#######################################
# read in CPF library domains
#######################################
read_cpf -library synth.cpf
check_library
…
elaborate ${TOPMODULE}
#######################################
# read in CPF file
#######################################
read_cpf synth.cpf
…
check_design -unresolved
report timing -mode PM1 -lint
report timing -mode PM2 –lint
…
#########################################
# Synthesize to Technology Mapped Gates
#########################################
synthesize -to_mapped -eff high
reload_cpf
commit_cpf
…

## Slide 9: CPF Tutorial
We now move on to the physical implementation. Before specifying floorplan, we Load & Commit the CPF file:

## Slide 10: CPF Tutorial
We use hierarchical floorplanning , so we move power domain macro modules
Encounter leaves a row and column between different power domains

## Slide 11: CPF Tutorial
Go through the regular flow of adding power rings for the PRIMARY rails only
Add power switches in respective power domain

## Slide 12: CPF Tutorial
Specify switch topology, switch topology should be determined by estimated header sizing and header layout. To understand more about this, please refer to our Final Report

## Slide 13: CPF Tutorial
Specify Global Net Connections
Specify virtual rail connections
Specifically, specify which rail connects to each power domain
Also specify which rails power switches will be switching between

## Slide 14: CPF Tutorial
Continue to do special route of power nets as you would in regular flow
Rest of flow is same as SOC place and route flow
CPF commands can be integrated into Encounter command script, so CPF retains the convenience synthesis flow brings us, with powerful flexibility for low power design

## Slide 15: CPF Tutorial
A snapshot of a completed, power-gated ALU within a microprocessor, with the power-gated ALU in the upper-left corner